## Slide 1
General License Course
Chapter 5.5
HF Station Installation

## Slide 2
Mobile Installations
Mobile 100 W HF rigs require 20 A or more current at 12 V minimum
Power connections go directly to the battery using heavy gauge wire with fuses in both the positive and negative leads*
Do not use a cigarette lighter socket! Wiring not rated for the current drawn, socket may be damaged
Do not assume that the vehicle’s metal chassis is a suitable dc ground connection
* see next slide...

## Slide 3
Mobile Installations
Connect the radio power ground (negative) either directly to the battery or where the battery ground strap attaches to the engine block or vehicle chassis. This is where the battery management system negative connection is made in modern vehicles. This connection must not be bypassed (by your antenna ground connection). Connecting the radio negative lead directly to the battery may also interfere with the operation of any special installation practices used by the manufacturer with respect to galvanic corrosion in aluminum-bodied vehicles, thus voiding the warranty.

## Slide 4
Mobile HF Antennas
The most significant limitation of mobile HF operating is the antenna system
Electrically short, very inefficient
The 40, 60, 80/75, 160 meter bands are particularly challenging because of electrically short antennas

## Slide 5
Mobile HF Antennas
The entire vehicle is part of the antenna system
Use the most efficient antenna you can
Make sure RF ground connections to the vehicle are solid
Mount the antenna where it is as clear as possible of metal surfaces

## Slide 6
Mobile Interference - Sources
Ignition noise from arcs at the spark plugs
Vehicle’s onboard control computers
Electric fuel pumps and windows
Battery charging systems
All three are correct!
Manufacturer service bulletins can help deal with interference and noise problems without voiding warranties

## Slide 7
Home Station Grounding
AC safety ground wiring can act more like an antenna than a ground - Separate RF bonding is intended to keep all equipment grounds at the same RF voltage
Bond all equipment enclosures/grounds together!
Minimizes “hot spots” (high RF voltage)
Prevents hazardous voltages from appearing on the chassis
Reduces RF current flowing between pieces of equipment which can cause audio distortion or improper operation

## Slide 8
Grounding & Bonding
During digital operation, RF being picked up on an audio cable (between the computer and transceiver) can cause:
  Audio distortion resulting in transmitted signal distortion or erratic operation of computer interfaces
  The transmitter to Key/Un-key improperly (when using VOX)
  Garbled signals causing data loss or connection timeout
(demo later)

## Slide 9
Grounding & Bonding
External ground connections – make the connection as short as possible with heavy wire or strap
As ground wire length approaches an odd number of ¼-wavelengths, it presents a high impedance at that frequency (it is resonant) which allows RF voltages on equipment enclosures and connecting cables - beware of RF burns!

## Slide 10
Grounding & Bonding
Ground loops are created when a continuous current path exists through enclosures and cables. Loops are nearly impossible to avoid.
The loops act as single-turn inductors picking up voltages from magnetic fields. The result can be a “hum” or “buzz” on your transmitted signal, on audio signals, or interference with control or data signals
Minimize the effect of ground loops by minimizing loop area and connecting all equipment grounds together at a single point.

## Slide 11
Grounding & Bonding
Good practice is to provide good bonding and make earth connections short

## Slide 12
RF Interference
Fundamental overload – radio or TV receivers unable to reject a strong signal. This causes distortion or inability to receive the desired signal.
Cure – prevent the offending signal from entering the equipment by using filters in the path of the signal.

## Slide 13
RF Interference
Two types: Common-mode and direct pickup (or direct detection) – The signal is picked up as common-mode current on the outside of cable shields or on all conductors of an unshielded connection
Power cords, speaker leads, telephone cable
Conducted into the equipment where it causes erratic operation or audio noise
Cure – block current with RF chokes (Ferrite beads) to increase the impedance of the common-mode noise path

## Slide 14
C:\Users\ai2n\Videos\General Course - Videos\Ferrite_Noise_Reduction.wmv
Ferrites (SDR-Spectrum Analyzer)
(note the “waterfall” display)
RF chokes made from ferrite cores and beads block common-mode RF current

## Slide 15
RF Interference
Distorted speech is heard from an audio device or telephone if there is interference from a nearby single-sideband phone transmitter
On-and-off humming or clicking is one effect that a nearby CW transmitter may have on an audio device or telephone system

## Slide 16
RF Interference
Harmonics – spurious emissions from an amateur station may be received by radio or TV equipment
Cure – use a low-pass filter at the transmitter to remove the spurious emissions (or a hi-pass filter at the device)
The filter’s impedance must closely match the characteristic impedance of the feed line
RFI to cable TV may be due to bad connectors allowing external signals to get in (or out – also known as cable leakage)

## Slide 17
RF Interference
Rectification – Poor contacts between conductors picking up RF signals can create a mixer and mixing products from the signals – Cure: repair the contact or connection
Arcing – arcing at a poor electrical connection creates interference over a wide frequency range, typically from power-line hardware
  May require the power company to make the necessary repairs

## Slide 18
RF Interference Suppression
Bypass capacitors CAN be useful in reducing RF interference to audio frequency devices - but -
This is not recommended for modern, solid-state audio amplifier outputs – it may cause them to become unstable (oscillate) and damage the amplifier.
  Use RF chokes first
  Twisted-pair speaker cable also helps.
  Only try bypass capacitors as a last resort on device power and non-audio signal connections

## Slide 19
RF Interference
Intermodulation: Poor contact between conductors picking up two RF signals (f1 and f2) can create a non-linear connection that acts as a mixer and produces mixing products which may interfere with reception
Cure: find and repair the faulty connection
Example: Strong, local AM broadcast stations at 830 and 1000 kHz would generate mixing products at 170 kHz (LF band) and 1830 kHz (MF band in the 160 meter amateur band)

## Slide 20
Remember that intermodulation refers to mixing products (f1 + f2). The odd-order intermodulation refers to a harmonic (i.e., a spurious harmonic emission).
Since odd-order harmonics are closest to the original (fundamental) frequency, they refer to the second harmonic of F1 (instead of the 3rd, 4th, etc.).
The frequency of this 2nd harmonic is represented by the formula (2 × f1 or 2F1)
So, the two intermodulation products of F1 and F2, where F1 is really the 2nd harmonic of F1 would be the sum and difference, 2F1 + F2 and 2F1 – F2.
Which of the following is an odd-order intermodulation product
of frequencies F1 and F2? Answer: 2F1 – F2
Odd-Order Harmonics

## Slide 21
Take Quiz 1

## Slide 22
G4C01 - Which of the following might be useful in reducing RF interference to audio frequency circuits?
A. Bypass inductor
B. Bypass capacitor
C. Forward-biased diode
D. Reverse-biased diode

## Slide 23
G4C01 - Which of the following might be useful in reducing RF interference to audio frequency circuits?
A. Bypass inductor
B. Bypass capacitor
C. Forward-biased diode
D. Reverse-biased diode

## Slide 24
G4C02 - Which of the following could be a cause of interference covering a wide range of frequencies?
A. Not using a balun or line isolator to feed balanced antennas
B. Lack of rectification of the transmitter's signal in power conductors
C. Arcing at a poor electrical connection
D. Using a balun to feed an unbalanced antenna

## Slide 25
G4C02 - Which of the following could be a cause of interference covering a wide range of frequencies?
A. Not using a balun or line isolator to feed balanced antennas
B. Lack of rectification of the transmitter's signal in power conductors
C. Arcing at a poor electrical connection
D. Using a balun to feed an unbalanced antenna

## Slide 26
G4C03 - What sound is heard from an audio device experiencing RF interference from a single sideband phone transmitter?
A. A steady hum whenever the transmitter is on the air
B. On-and-off humming or clicking
C. Distorted speech
D. Clearly audible speech

## Slide 27
G4C03 - What sound is heard from an audio device experiencing RF interference from a single sideband phone transmitter?
A. A steady hum whenever the transmitter is on the air
B. On-and-off humming or clicking
C. Distorted speech
D. Clearly audible speech

## Slide 28
G4C04 - What sound is heard from an audio device experiencing RF interference from a CW transmitter?
A. On-and-off humming or clicking
B. A CW signal at a nearly pure audio frequency
C. A chirpy CW signal
D. Severely distorted audio

## Slide 29
G4C04 - What sound is heard from an audio device experiencing RF interference from a CW transmitter?
A. On-and-off humming or clicking
B. A CW signal at a nearly pure audio frequency
C. A chirpy CW signal
D. Severely distorted audio

## Slide 30
G4C05 - What is a possible cause of high voltages that produce RF burns?
A. Flat braid rather than round wire has been used for the ground wire
B. Insulated wire has been used for the ground wire
C. The ground rod is resonant
D. The ground wire has high impedance on that frequency

## Slide 31
G4C05 - What is a possible cause of high voltages that produce RF burns?
A. Flat braid rather than round wire has been used for the ground wire
B. Insulated wire has been used for the ground wire
C. The ground rod is resonant
D. The ground wire has high impedance on that frequency

## Slide 32
G4C06 - What is a possible effect of a resonant ground connection?
A. Overheating of ground straps
B. Corrosion of the ground rod
C. High RF voltages on the enclosures of station equipment
D. A ground loop

## Slide 33
G4C06 - What is a possible effect of a resonant ground connection?
A. Overheating of ground straps
B. Corrosion of the ground rod
C. High RF voltages on the enclosures of station equipment
D. A ground loop

## Slide 34
G4C08 - Which of the following would reduce RF interference caused by common-mode current on an audio cable?
A. Place a ferrite choke on the cable
B. Connect the center conductor to the shield of all cables to short circuit the RFI signal
C. Ground the center conductor of the audio cable causing the interference
D. Add an additional insulating jacket to the cable

## Slide 35
G4C08 - Which of the following would reduce RF interference caused by common-mode current on an audio cable?
A. Place a ferrite choke on the cable
B. Connect the center conductor to the shield of all cables to short circuit the RFI signal
C. Ground the center conductor of the audio cable causing the interference
D. Add an additional insulating jacket to the cable

## Slide 36
G4C09 - How can the effects of ground loops be minimized?
A. Connect all ground conductors in series
B. Connect the AC neutral conductor to the ground wire
C. Avoid using lock washers and star washers when making ground connections
D. Bond equipment enclosures together

## Slide 37
G4C09 - How can the effects of ground loops be minimized?
A. Connect all ground conductors in series
B. Connect the AC neutral conductor to the ground wire
C. Avoid using lock washers and star washers when making ground connections
D. Bond equipment enclosures together

## Slide 38
G4C10 - What could be a symptom caused by a ground loop in your station's audio connections?
A. You receive reports of "hum" on your station's transmitted signal
B. The SWR reading for one or more antennas is suddenly very high
C. An item of station equipment starts to draw excessive amounts of current
D. You receive reports of harmonic interference from your station

## Slide 39
G4C10 - What could be a symptom caused by a ground loop in your station's audio connections?
A. You receive reports of "hum" on your station's transmitted signal
B. The SWR reading for one or more antennas is suddenly very high
C. An item of station equipment starts to draw excessive amounts of current
D. You receive reports of harmonic interference from your station

## Slide 40
G4C11 - What technique helps to minimize RF "hot spots" in an amateur station?
A. Building all equipment in a metal enclosure
B. Using surge suppressor power outlets
C. Bonding all equipment enclosures together
D. Placing low-pass filters on all feed lines

## Slide 41
G4C11 - What technique helps to minimize RF "hot spots" in an amateur station?
A. Building all equipment in a metal enclosure
B. Using surge suppressor power outlets
C. Bonding all equipment enclosures together
D. Placing low-pass filters on all feed lines

## Slide 42
G4C12 - Why must all metal enclosures of station equipment be grounded?
A. It prevents a blown fuse in the event of an internal short circuit
B. It prevents signal overload
C. It ensures that the neutral wire is grounded
D. It ensures that hazardous voltages cannot appear on the chassis

## Slide 43
G4C12 - Why must all metal enclosures of station equipment be grounded?
A. It prevents a blown fuse in the event of an internal short circuit
B. It prevents signal overload
C. It ensures that the neutral wire is grounded
D. It ensures that hazardous voltages cannot appear on the chassis

## Slide 44
G4E03 - Which of the following direct, fused power connections would be the best for a 100-watt HF mobile installation?
A. To the battery using heavy-gauge wire
B. To the alternator or generator using heavy-gauge wire
C. To the battery using insulated heavy duty balanced transmission line
D. To the alternator or generator using insulated heavy duty balanced transmission line

## Slide 45
G4E03 - Which of the following direct, fused power connections would be the best for a 100-watt HF mobile installation?
A. To the battery using heavy-gauge wire
B. To the alternator or generator using heavy-gauge wire
C. To the battery using insulated heavy duty balanced transmission line
D. To the alternator or generator using insulated heavy duty balanced transmission line

## Slide 46
G4E04 - Why should DC power for a 100-watt HF transceiver not be supplied by a vehicle's auxiliary power socket?
A. The socket is not wired with an RF-shielded power cable
B. The socket's wiring may be inadequate for the current drawn by the transceiver
C. The DC polarity of the socket is reversed from the polarity of modern HF transceivers
D. Drawing more than 50 watts from this socket could cause the engine to overheat

## Slide 47
G4E04 - Why should DC power for a 100-watt HF transceiver not be supplied by a vehicle's auxiliary power socket?
A. The socket is not wired with an RF-shielded power cable
B. The socket's wiring may be inadequate for the current drawn by the transceiver
C. The DC polarity of the socket is reversed from the polarity of modern HF transceivers
D. Drawing more than 50 watts from this socket could cause the engine to overheat

## Slide 48
G4E05 - Which of the following most limits an HF mobile installation?
A. "Picket fencing"
B. The wire gauge of the DC power line to the transceiver
C. Efficiency of the electrically short antenna
D. FCC rules limiting mobile output power on the 75-meter band

## Slide 49
G4E05 - Which of the following most limits an HF mobile installation?
A. "Picket fencing"
B. The wire gauge of the DC power line to the transceiver
C. Efficiency of the electrically short antenna
D. FCC rules limiting mobile output power on the 75-meter band

## Slide 50
G4E07 - Which of the following may cause receive interference to an HF transceiver installed in a vehicle?
A. The battery charging system
B. The fuel delivery system
C. The control computers
D. All these choices are correct

## Slide 51
G4E07 - Which of the following may cause receive interference to an HF transceiver installed in a vehicle?
A. The battery charging system
B. The fuel delivery system
C. The control computers
D. All these choices are correct

## Slide 52
G6B10 - How does a ferrite bead or core reduce common-mode RF current on the shield of a coaxial cable?
A. By creating an impedance in the current's path
B. It converts common-mode current to differential mode current
C. By creating an out-of-phase current to cancel the common-mode current
D. Ferrites expel magnetic fields

## Slide 53
G6B10 - How does a ferrite bead or core reduce common-mode RF current on the shield of a coaxial cable?
A. By creating an impedance in the current's path
B. It converts common-mode current to differential mode current
C. By creating an out-of-phase current to cancel the common-mode current
D. Ferrites expel magnetic fields

## Slide 54
G8B05 - Which intermodulation products are closest to the original signal frequencies?
A. Second harmonics
B. Even-order
C. Odd-order
D. Intercept point

## Slide 55
G8B05 - Which intermodulation products are closest to the original signal frequencies?
A. Second harmonics
B. Even-order
C. Odd-order
D. Intercept point

## Slide 56
G8B12 - What process combines two signals in a non-linear circuit to produce unwanted spurious outputs?
A. Intermodulation
B. Heterodyning
C. Detection
D. Rolloff

## Slide 57
G8B12 - What process combines two signals in a non-linear circuit to produce unwanted spurious outputs?
A. Intermodulation
B. Heterodyning
C. Detection
D. Rolloff

## Slide 58
G8B13 - Which of the following is an odd-order intermodulation product of frequencies F1 and F2?
A. 5F1-3F2
B. 3F1-F2
C. 2F1-F2
D. All these choices are correct

## Slide 59
G8B13 - Which of the following is an odd-order intermodulation product of frequencies F1 and F2?
A. 5F1-3F2
B. 3F1-F2
C. 2F1-F2
D. All these choices are correct

## Slide 60
General License Course
Chapter 6.1 and 6.2
Basics of Digital Modes
and
Character-Based Modes

## Slide 61
Digital Modes
Radioteletype (RTTY) – invented in the ‘30s, originally used mechanical teleprinters but migrated to computer sound cards
RTTY is popular on all the HF amateur bands (100% duty cycle)
PSK31 and FT8 – good weak signal modes allowing low transmitter power
and very narrow bandwidth (computer sound card)

## Slide 62
Digital Modes and Where to Find Them
Band Notes
(Meters) (MHz)
160 1.800 – 1.810
80 3.570 - 3.600
60 Data emission not permitted
40 7.080 - 7.125 RTTY DX calling frequency 7.040 MHz
30 10.130 - 10.150
20 14.070 - 14.100 *
(PSK31 calling frequency 14.070 MHz, below RTTY seqment)
17 18.100 - 18.110
15 21.070 - 21.110
12 24.920 - 24.930
10 28.070 - 28.150
* but stay clear of 14.100 Beacon frequency

## Slide 63
FSK – AFSK
Frequency Shift Keying (FSK) – the frequency of the transmitter’s VFO (oscillator) is controlled directly by a digital control signal from the computer
Audio frequency shift keying (AFSK) – audio tones are used to modulate an SSB or FM transmitter through the microphone or other audio input
  Audio must be kept free of noise
  ALC and compression must not be used to prevent distortion

## Slide 64
Frequency Shift Keying (FSK)
RTTY signal – two different tones shifting from one frequency to another
The rapidly changing tones are called mark and space
7079.830 kHz
7080.000 kHz
Space represents 0 Mark represents 1 170 Hz shift typical
Oldest digital mode – still very popular.

## Slide 65
Radioteletype (RTTY)
RTTY uses the Baudot code, which represents (encodes) each text character as a sequence of 5 bits
An initial bit (the start bit) and an inter-character pause (the stop bit) are used to synchronize the transmitting and receiving stations - these bits are NOT included in the 5 bit character sequence
So: Baudot code is a 5-bit code with additional start and stop bits

## Slide 66
PSK31
The “31” stands for the symbol rate of the protocol, actually 31.25 baud
BPSK* uses a variable length code called Varicode that assigns shorter codes to common characters and longer codes for others (the number of data bits required to transmit a character varies)
Capital letters and punctuation characters take more bits and thus slow down transmission
*Note: BPSK31 = Binary PSK31,
the most common form of PSK31

## Slide 67
QPSK31
QPSK31 (Quadrature PSK) sends two audio tones, allowing 4 (0, 90, 180, 270 degree) phase shift combinations
  This encoding allows some error correction
  It is, however, sideband sensitive
  It occupies about the same bandwidth as BPSK31
All Three...

## Slide 68
PSK31
C:\Users\ai2n\Videos\General Course - Videos\psk-31 demo.wmv

## Slide 69
Digital voice modes are regulated as voice emissions by the FCC. Examples include Icom’s D-STAR, Yaesu’s System Fusion, AOR’s digital voice system, and DMR.
Digital Voice Modes

## Slide 70
Take Quiz 2

## Slide 71
G2E08 - In what segment of the 20-meter band are most digital mode operations commonly found?
A. At the bottom of the slow-scan TV segment, near 14.230 MHz
B. At the top of the SSB phone segment, near 14.325 MHz
C. In the middle of the CW segment, near 14.100 MHz
D. Between 14.070 MHz and 14.100 MHz

## Slide 72
G2E08 - In what segment of the 20-meter band are most digital mode operations commonly found?
A. At the bottom of the slow-scan TV segment, near 14.230 MHz
B. At the top of the SSB phone segment, near 14.325 MHz
C. In the middle of the CW segment, near 14.100 MHz
D. Between 14.070 MHz and 14.100 MHz

## Slide 73
G8A01 - How is direct binary FSK modulation generated?
A. By keying an FM transmitter with a sub-audible tone
B. By changing an oscillator's frequency directly with a digital control signal
C. By using a transceiver's computer data interface protocol to change frequencies
D. By reconfiguring the CW keying input to act as a tone generator

## Slide 74
G8A01 - How is direct binary FSK modulation generated?
A. By keying an FM transmitter with a sub-audible tone
B. By changing an oscillator's frequency directly with a digital control signal
C. By using a transceiver's computer data interface protocol to change frequencies
D. By reconfiguring the CW keying input to act as a tone generator

## Slide 75
G8C11 - How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified?
A. Dot and dash
B. On and off
C. High and low
D. Mark and space

## Slide 76
G8C11 - How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified?
A. Dot and dash
B. On and off
C. High and low
D. Mark and space

## Slide 77
G8C16 - Which of the following provide digital voice modes?
A. WSPR, MFSK16, and EasyPAL
B. FT8, FT4, and FST4
C. Winlink, PACTOR II, and PACTOR III
D. DMR, D-STAR, and SystemFusion

## Slide 78
G8C16 - Which of the following provide digital voice modes?
A. WSPR, MFSK16, and EasyPAL
B. FT8, FT4, and FST4
C. Winlink, PACTOR II, and PACTOR III
D. DMR, D-STAR, and SystemFusion

## Slide 79
G2E06 - What is the most common frequency shift for RTTY emissions in the amateur HF bands?
A. 85 Hz
B. 170 Hz
C. 425 Hz
D. 850 Hz

## Slide 80
G2E06 - What is the most common frequency shift for RTTY emissions in the amateur HF bands?
A. 85 Hz
B. 170 Hz
C. 425 Hz
D. 850 Hz

## Slide 81
G8A06 - Which of the following is characteristic of QPSK31?
A. It is sideband sensitive
B. Its encoding provides error correction
C. Its bandwidth is approximately the same as BPSK31
D. All these choices are correct

## Slide 82
G8A06 - Which of the following is characteristic of QPSK31?
A. It is sideband sensitive
B. Its encoding provides error correction
C. Its bandwidth is approximately the same as BPSK31
D. All these choices are correct

## Slide 83
G8C04 - Which of the following describes Baudot code?
A. A 7-bit code with start, stop, and parity bits
B. A code using error detection and correction
C. A 5-bit code with additional start and stop bits
D. A code using SELCAL and LISTEN

## Slide 84
G8C04 - Which of the following describes Baudot code?
A. A 7-bit code with start, stop, and parity bits
B. A code using error detection and correction
C. A 5-bit code with additional start and stop bits
D. A code using SELCAL and LISTEN

## Slide 85
G8C08 - Which of the following statements is true about PSK31?
A. Upper case letters are sent with more power
B. Upper case letters use longer Varicode bit sequences and thus slow down transmission
C. Error correction is used to ensure accurate message reception
D. Higher power is needed as compared to RTTY for similar error rates

## Slide 86
G8C08 - Which of the following statements is true about PSK31?
A. Upper case letters are sent with more power
B. Upper case letters use longer Varicode bit sequences and thus slow down transmission
C. Error correction is used to ensure accurate message reception
D. Higher power is needed as compared to RTTY for similar error rates

## Slide 87
G8C12 - Which type of code is used for sending characters in a PSK31 signal?
A. Varicode
B. Viterbi
C. Volumetric
D. Binary

## Slide 88
G8C12 - Which type of code is used for sending characters in a PSK31 signal?
A. Varicode
B. Viterbi
C. Volumetric
D. Binary

## Slide 89
General License Course
Chapter 6.3
Packet-Based Modes

## Slide 90
Packet Radio Basics
Packet refers to the transmission of data in structured groups
Header – at the start of the packet – contains:
  Synchronization patterns for the receiver
  Control, routing and handling information
  Error detection and correction information

## Slide 91
Packet - Error Correction
Forward error correction (FEC) –includes additional redundant information with the data being transmitted
Automatic Repeat reQuest (ARQ) – the protocol requires that a packet with errors in the data be retransmitted
Uses ACK (rcvd OK) and NAK (error detected – retransmit previous packet) messages to the sending station

## Slide 92
Packet - Error Correction
ARQ protocols are designed to transfer data between two stations
An ACK or NAK response to the sending station can only be received from one receiving station
You can't “break in” to an ongoing contact between two stations using an ARQ mode (PACTOR or WINMOR)

## Slide 93
Packet - Error Correction
Monitoring or “MON” mode – stations can listen to the ARQ conversation (without connecting) and receive the data without retransmission of “bad” packets
Monitoring mode allows you to determine if a frequency is occupied
PACTOR and WINMOR are ARQ protocols – the preferred method of HF data transmission for the popular Winlink email system

## Slide 94
PACTOR and WINLINK
PACTOR stands for PACket Teletype Over Radio
WINMOR (WINLINK) stands for Windows Messaging Over Radio and can also use the Internet if an RF pathway is not available. It’s a form to Packet Radio
Both modes use advanced modulation techniques, including error correction and automatic communication control

## Slide 95
WINLINK
Enables transferring of email messages & digital files on HF bands
Winlink isn’t a mode … it’s a gateway communication system utilizing Winlink Remote Message Servers
Uses internet to connect its email servers with gateway and mailbox stations around the world on HF, VHF and UHF
Winlink stations do not connect directly with the internet, but provide a means
(via relay) for stations out of local internet connection range
Even without internet connectivity, Winlink Express can act as standalone mailbox stations or communicate directly with each other
On HF, WINLINK uses PACTOR and VARA digital protocols
(VARA is the more popular)
VARA is software developed by EA5HVK Software

## Slide 96
Newer Packet Modes
FT8* and WSPR (from WSJT-X family) use precisely timed 8-tone FSK modulation and sophisticated error correction to permit use at very low signal-to-noise ratios
This requires computer time accuracy within ~1 second of standard time
*FT8 = 8-tone

## Slide 97
Newer Packet Modes
An FT8 signal report of “+3” represents a signal-to-noise ratio of +3 dB in a 2.5kHz bandwidth
FT8 is commonly found between 14.074-14.077 MHz on 20 meters
When on FT8 observe the waterfall display and select an unused audio frequency on which to transmit. When answering a CQ, be sure to call during the alternate (opposite) time slot to the station being called.
FT8 Video – coming soon!

## Slide 98
Newer Packet Modes
Because of time and bandwidth considerations, FT8 can exchange a limited amount of information, generally call signs, grid locators and signal reports. It is an open-source mode, so variations other than WSJT may behave differently
WSPR (Whisper) is designed to assess HF propagation at very low signal-to-noise ratios. It does not support two-way communication and acts as a beacon. Successful reception can be reported on websites such as wsprnet.org

## Slide 99
Amateur Radio Wireless Networks
Certain wireless networking frequencies overlap with amateur bands (see Table 6.2)
Amateurs are able to use them for many of the same purposes that unlicensed users are able to (text messages, Voice Over IP, email, etc.)
If you operate a wireless network on FCC Part 97 frequencies, you must comply with the prohibitions on encryption
Hams use two basic network topologies; mesh and star configurations
An advantage of the mesh networking topology is that if one node fails, a packet may be able to find its destination by routing through another available node

## Slide 100
Table 6.2: Wireless Networking Frequencies

## Slide 101
AREDN (AMATEUR RADIO EMERGENCY DATA NETWORK)
A mesh network providing high-speed data services
Uses commercially available routers in the 900 MHz, 2.4, 3.4, and 5.8 GHz amateur bands
Supported device list at:
https://www.arednmesh.org/content/supported-platform-matrix
Generally used during emergencies or to support community events like road races, parades, and other large gatherings

## Slide 102
Take Quiz 3

## Slide 103
G2E02 - What is VARA?
A. A low signal-to-noise digital mode used for EME (moonbounce)
B. A digital protocol used with Winlink
C. A radio direction finding system used on VHF and UHF
D. A DX spotting system using a network of software defined radios

## Slide 104
G2E02 - What is VARA?
A. A low signal-to-noise digital mode used for EME (moonbounce)
B. A digital protocol used with Winlink
C. A radio direction finding system used on VHF and UHF
D. A DX spotting system using a network of software defined radios

## Slide 105
G2E04 - Which of the following is good practice when choosing a transmitting frequency to answer a station calling CQ using FT8?
A. Always call on the station's frequency
B. Call on any frequency in the waterfall except the station's frequency
C. Find a clear frequency during the same time slot as the calling station
D. Find a clear frequency during the alternate time slot to the calling station

## Slide 106
G2E04 - Which of the following is good practice when choosing a transmitting frequency to answer a station calling CQ using FT8?
A. Always call on the station's frequency
B. Call on any frequency in the waterfall except the station's frequency
C. Find a clear frequency during the same time slot as the calling station
D. Find a clear frequency during the alternate time slot to the calling station

## Slide 107
G2E07 - Which of the following is required when using FT8?
A. A special hardware modem
B. Computer time accurate to within approximately 1 second
C. Receiver attenuator set to -12 dB
D. A vertically polarized antenna

## Slide 108
G2E07 - Which of the following is required when using FT8?
A. A special hardware modem
B. Computer time accurate to within approximately 1 second
C. Receiver attenuator set to -12 dB
D. A vertically polarized antenna

## Slide 109
G2E09 - How do you join a contact between two stations using the PACTOR protocol?
A. Send broadcast packets containing your call sign while in MONITOR mode
B. Transmit a steady carrier until the PACTOR protocol times out and disconnects
C. Joining an existing contact is not possible, PACTOR connections are limited to two stations
D. Send a NAK code

## Slide 110
G2E09 - How do you join a contact between two stations using the PACTOR protocol?
A. Send broadcast packets containing your call sign while in MONITOR mode
B. Transmit a steady carrier until the PACTOR protocol times out and disconnects
C. Joining an existing contact is not possible, PACTOR connections are limited to two stations
D. Send a NAK code

## Slide 111
G2E11 - What is the primary purpose of an Amateur Radio Emergency Data Network (AREDN) mesh network?
A. To provide FM repeater coverage in remote areas
B. To provide real time propagation data by monitoring amateur radio transmissions worldwide
C. To provide high-speed data services during an emergency or community event
D. To provide DX spotting reports to aid contesters and DXers

## Slide 112
G2E11 - What is the primary purpose of an Amateur Radio Emergency Data Network (AREDN) mesh network?
A. To provide FM repeater coverage in remote areas
B. To provide real time propagation data by monitoring amateur radio transmissions worldwide
C. To provide high-speed data services during an emergency or community event
D. To provide DX spotting reports to aid contesters and DXers

## Slide 113
G2E12 - Which of the following describes Winlink?
A. An amateur radio wireless network to send and receive email on the internet
B. A form of Packet Radio
C. A wireless network capable of both VHF and HF band operation
D. All these choices are correct

## Slide 114
G2E12 - Which of the following describes Winlink?
A. An amateur radio wireless network to send and receive email on the internet
B. A form of Packet Radio
C. A wireless network capable of both VHF and HF band operation
D. All these choices are correct

## Slide 115
G2E13 - What is another name for a Winlink Remote Message Server?
A. Terminal Node Controller
B. Gateway
C. RJ-45
D. Printer/Server

## Slide 116
G2E13 - What is another name for a Winlink Remote Message Server?
A. Terminal Node Controller
B. Gateway
C. RJ-45
D. Printer/Server

## Slide 117
G2E15 - Which of the following is a common location for FT8?
A. Anywhere in the voice portion of the band
B. Anywhere in the CW portion of the band
C. Approximately 14.074 MHz to 14.077 MHz
D. Approximately 14.110 MHz to 14.113 MHz

## Slide 118
G2E15 - Which of the following is a common location for FT8?
A. Anywhere in the voice portion of the band
B. Anywhere in the CW portion of the band
C. Approximately 14.074 MHz to 14.077 MHz
D. Approximately 14.110 MHz to 14.113 MHz

## Slide 119
G8A09 - What type of modulation is used by FT8?
A. 8-tone frequency shift keying
B. Vestigial sideband
C. Amplitude compressed AM
D. 8-bit direct sequence spread spectrum

## Slide 120
G8A09 - What type of modulation is used by FT8?
A. 8-tone frequency shift keying
B. Vestigial sideband
C. Amplitude compressed AM
D. 8-bit direct sequence spread spectrum

## Slide 121
G8A12 - What is QPSK modulation?
A. Modulation using quasi-parallel to serial conversion to reduce bandwidth
B. Modulation using quadra-pole sideband keying to generate spread spectrum signals
C. Modulation using Fast Fourier Transforms to generate frequencies at the first, second, third, and fourth harmonics of the carrier frequency to improve noise immunity
D. Modulation in which digital data is transmitted using 0-, 90-, 180- and 270-degrees phase shift to represent pairs of bits

## Slide 122
G8A12 - What is QPSK modulation?
A. Modulation using quasi-parallel to serial conversion to reduce bandwidth
B. Modulation using quadra-pole sideband keying to generate spread spectrum signals
C. Modulation using Fast Fourier Transforms to generate frequencies at the first, second, third, and fourth harmonics of the carrier frequency to improve noise immunity
D. Modulation in which digital data is transmitted using 0-, 90-, 180- and 270-degrees phase shift to represent pairs of bits

## Slide 123
G8C02 - Which digital mode is used as a low-power beacon for assessing HF propagation?
A. WSPR
B. MFSK16
C. PSK31
D. SSB-SC

## Slide 124
G8C02 - Which digital mode is used as a low-power beacon for assessing HF propagation?
A. WSPR
B. MFSK16
C. PSK31
D. SSB-SC

## Slide 125
G8C03 - What part of a packet radio frame contains the routing and handling information?
A. Directory
B. Preamble
C. Header
D. Trailer

## Slide 126
G8C03 - What part of a packet radio frame contains the routing and handling information?
A. Directory
B. Preamble
C. Header
D. Trailer

## Slide 127
G8C05 - In an ARQ mode, what is meant by a NAK response to a transmitted packet?
A. Request retransmission of the packet
B. Packet was received without error
C. Receiving station connected and ready for transmissions
D. Entire file received correctly

## Slide 128
G8C05 - In an ARQ mode, what is meant by a NAK response to a transmitted packet?
A. Request retransmission of the packet
B. Packet was received without error
C. Receiving station connected and ready for transmissions
D. Entire file received correctly

## Slide 129
G8C07 - Which of the following narrow-band digital modes can receive signals with very low signal-to-noise ratios?
A. MSK144
B. FT8
C. AMTOR
D. MFSK32

## Slide 130
G8C07 - Which of the following narrow-band digital modes can receive signals with very low signal-to-noise ratios?
A. MSK144
B. FT8
C. AMTOR
D. MFSK32

## Slide 131
G8C09 - Which is true of mesh network microwave nodes?
A. Having more nodes increases signal strengths
B. If one node fails, a packet may still reach its target station via an alternate node
C. Links between two nodes in a network may have different frequencies and bandwidths
D. More nodes reduce overall microwave out of band interference

## Slide 132
G8C09 - Which is true of mesh network microwave nodes?
A. Having more nodes increases signal strengths
B. If one node fails, a packet may still reach its target station via an alternate node
C. Links between two nodes in a network may have different frequencies and bandwidths
D. More nodes reduce overall microwave out of band interference

## Slide 133
G8C10 - How does forward error correction (FEC) allow the receiver to correct data errors?
A. By controlling transmitter output power for optimum signal strength
B. By using the Varicode character set
C. By transmitting redundant information with the data
D. By using a parity bit with each character

## Slide 134
G8C10 - How does forward error correction (FEC) allow the receiver to correct data errors?
A. By controlling transmitter output power for optimum signal strength
B. By using the Varicode character set
C. By transmitting redundant information with the data
D. By using a parity bit with each character

## Slide 135
G8C15 - What does an FT8 signal report of +3 mean?
A. The signal is 3 times the noise level of an equivalent SSB signal
B. The signal is S3 (weak signals)
C. The signal-to-noise ratio is equivalent to +3dB in a 2.5 kHz bandwidth
D. The signal is 3 dB over S9

## Slide 136
G8C15 - What does an FT8 signal report of +3 mean?
A. The signal is 3 times the noise level of an equivalent SSB signal
B. The signal is S3 (weak signals)
C. The signal-to-noise ratio is equivalent to +3dB in a 2.5 kHz bandwidth
D. The signal is 3 dB over S9

## Slide 137
General License Course
Chapter 6.4
Receiving and Transmitting
Digital Modes

## Slide 138
Receiving and Transmitting Digital Modes
AFSK RTTY is transmitted as a LSB signal. Make sure audio levels are adequate (most common problem)
JT65, JT9, FT4, and FT8 use USB.
USB/LSB selected by convention for each mode.
Digital signals of the wrong baud rate, on the wrong sideband or with the mark and space frequencies reversed will not decode correctly because the relationship of the tones and the digital data will be inverted. (ALL THREE)
Know where your sidebands are with respect to the displayed frequency – stay in the band!

## Slide 139
Bandwidth of Digital Modes
The FCC rules define the bandwidth of a digital mode signal in the same way as any other signal
As the symbol rate of a digital signal increases, so does the bandwidth required to transmit that signal

## Slide 140
Bandwidth of Digital Modes
Bandwidth Comparison of Digital Modes
Mode Bandwidth (Hz)
FT8 50
PSK31 50
RTTY 200
MFSK16 300
JT65 350
DominoEX 524
Olivia 1000
WINMOR 1600
MT63 2000
PACTOR-III, -IV 2300
Bandwidths are approximate for the highest commonly
used symbol rate and are not specifications.
Stay away from band/sub-band edges!

## Slide 141
Transmitter Duty Cycle
Most amateur transmitters are not designed to operate at full power output for an extended time
RTTY, PSK31 – nearly 100% duty cycle
ARQ modes – less than 100% but still high
Reduce your transmitter power to about 50% of maximum output power for most digital modes

## Slide 142
Digital Mode Signal Quality
Excess audio levels causes distortion and splatter just as for voice modes
On a waterfall display, vertical lines to each side of the main signal represents a spurious emission (overmodulation) (more later…)
Distortion makes a signal harder to copy
Spurious emissions cause interference
Keep your data audio levels set correctly

## Slide 143
ALC and Digital Modes
Automatic Level Control (ALC) is used to prevent excessive drive to amplifier inputs
As it changes power levels, ALC can cause distortion of the original signal.
Distortion caused by ALC makes the signal harder to decode (distorts the signal) and creates spurious emissions
  Mild distortion caused by ALC is acceptable on voice modes

## Slide 144
ALC and Digital Modes
When using a digital mode, your ALC system should be either disabled or the microphone input level and gain turned down to the point where the ALC system does not activate
Monitor ALC during digital transmission (usually a meter function selection)

## Slide 145
Take Quiz 4

## Slide 146
G2E01 - Which mode is normally used when sending RTTY signals via AFSK with an SSB transmitter?
A. USB
B. DSB
C. CW
D. LSB

## Slide 147
G2E01 - Which mode is normally used when sending RTTY signals via AFSK with an SSB transmitter?
A. USB
B. DSB
C. CW
D. LSB

## Slide 148
G2E05 - What is the standard sideband for JT65, JT9, FT4, or FT8 digital signal when using AFSK?
A. LSB
B. USB
C. DSB
D. SSB

## Slide 149
G2E05 - What is the standard sideband for JT65, JT9, FT4, or FT8 digital signal when using AFSK?
A. LSB
B. USB
C. DSB
D. SSB

## Slide 150
G2E14 - What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
A. The mark and space frequencies may be reversed
B. You may have selected the wrong baud rate
C. You may be listening on the wrong sideband
D. All these choices are correct

## Slide 151
G2E14 - What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
A. The mark and space frequencies may be reversed
B. You may have selected the wrong baud rate
C. You may be listening on the wrong sideband
D. All these choices are correct

## Slide 152
G4A11 - Why should the ALC system be inactive when transmitting AFSK data signals?
A. ALC will invert the modulation of the AFSK mode
B. The ALC action distorts the signal
C. When using digital modes, too much ALC activity can cause the transmitter to overheat
D. All these choices are correct

## Slide 153
G4A11 - Why should the ALC system be inactive when transmitting AFSK data signals?
A. ALC will invert the modulation of the AFSK mode
B. The ALC action distorts the signal
C. When using digital modes, too much ALC activity can cause the transmitter to overheat
D. All these choices are correct

## Slide 154
G8B08 - Why is it important to know the duty cycle of the mode you are using when transmitting?
A. To aid in tuning your transmitter
B. Some modes have high duty cycles that could exceed the transmitter's average power rating
C. To allow time for the other station to break in during a transmission
D. To prevent overmodulation

## Slide 155
G8B08 - Why is it important to know the duty cycle of the mode you are using when transmitting?
A. To aid in tuning your transmitter
B. Some modes have high duty cycles that could exceed the transmitter's average power rating
C. To allow time for the other station to break in during a transmission
D. To prevent overmodulation

## Slide 156
G8B10 - What is the relationship between transmitted symbol rate and bandwidth?
A. Symbol rate and bandwidth are not related
B. Higher symbol rates require wider bandwidth
C. Lower symbol rates require wider bandwidth
D. Bandwidth is half the symbol rate

## Slide 157
G8B10 - What is the relationship between transmitted symbol rate and bandwidth?
A. Symbol rate and bandwidth are not related
B. Higher symbol rates require wider bandwidth
C. Lower symbol rates require wider bandwidth
D. Bandwidth is half the symbol rate

## Slide 158
G8C13 - What is indicated on a waterfall display by one or more vertical lines on either side of a data mode or RTTY signal?
A. Long path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation

## Slide 159
G8C13 - What is indicated on a waterfall display by one or more vertical lines on either side of a data mode or RTTY signal?
A. Long path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation

## Slide 160
General License Course
Chapter 6.5
Digital Operating Procedures

## Slide 161
Listening First
To avoid causing interference, the control operator:
  Must listen to the received audio or watch a waterfall-style display before transmitting
  It’s not enough to just check a BUSY light on a modem
  Follow good amateur practice and listen, listen, listen!

## Slide 162
Automatically Controlled Stations
“Automatically controlled digital station” is the FCC term for an unattended digital messaging system gateway station that transfers messages to and from the Internet.
Unmanned gateway and mailbox stations (connected to the Internet) monitor a published frequency awaiting stations to connect to them
They respond without requiring a human control operator

## Slide 163
Automatically Controlled Stations
Establishing a connection will vary with the equipment and mode being used
The contact starts with sending a CONNECT message (on the station's published frequency) to the station with which you want to connect
A training sequence then determines the best rate and modulation to use based on conditions
Once training is completed, a message can then be transferred

## Slide 164
Automatically Controlled Stations
Automatically controlled stations transmitting RTTY or data emissions may communicate with other automatically controlled digital stations anywhere where data is permitted in the 6 meter or shorter wavelength bands, and in specified segments of the 80 meter through 10 meter bands. (next slide)
To conduct communications with a digital station operating under automatic control outside the automatic control band segments the station initiating the contact must be under local or remote control.

## Slide 165
Automatically Controlled Stations
Automatic Control Band Segments for RTTY and Data
Band (Meters) Frequency range (MHz)
80 3.585-3.600
40 7.100-7.105
30 10.140-10.150
20 14.095-14.0995 and 14.1005-14.112
17 18.105-18.110
15 21.090-21.100
12 24.925-24.930
10 28.120-28.189

## Slide 166
Digital Contact Display
The waterfall displays the presence of signals as a series of lines, each representing a scan across the frequency range (horizontal) vs. time (vertical)
The strength of the signals is represented as the brightness, intensity, or color of the line at each frequency on the display
The display gives the impression of a “waterfall” as the data flows across the screen in successive scans

## Slide 167
C:\Users\ai2n\Videos\General Course - Videos\FT8 and Waterfall Demo.MOV
FT8 and Waterfall Demo

## Slide 168
PSK31 Waterfall

## Slide 169
Third Party Traffic
All FCC rules about third-party messages apply to digital transmissions – NO exemptions ever, anywhere, any mode
This includes all information included in email, digital images, or web pages transmitted via Amateur Radio
As always, commercial messages such as advertisements or pertaining to your business may not be transmitted via Amateur Radio

## Slide 170
Interfering Signals
PACTOR/VARA (Winlink) Symptoms of Interference:
  Failure to connect to target station
  Frequent retries or timeouts during data transfer
  Long pauses in message transmission
    ALL THREE...

## Slide 171
Interfering Signals
If requested ARQ mode retransmissions exceed a preset limit the connection will be dropped
Remember, the interference may be accidental; the other station may not hear your signal at all
  Use a different frequency
  Aim directional antennas in another direction

## Slide 172
Take Quiz 5

## Slide 173
G1E03 - What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments?
A. The station initiating the contact must be under local or remote control
B. The interrogating transmission must be made by another automatically controlled station
C. No third-party traffic may be transmitted
D. The control operator of the interrogating station must hold an Amateur Extra class license

## Slide 174
G1E03 - What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments?
A. The station initiating the contact must be under local or remote control
B. The interrogating transmission must be made by another automatically controlled station
C. No third-party traffic may be transmitted
D. The control operator of the interrogating station must hold an Amateur Extra class license

## Slide 175
G1E09 - Under what circumstances are messages that are sent via digital modes exempt from Part 97 third-party rules that apply to other modes of communication?
A. Under no circumstances
B. When messages are encrypted
C. When messages are not encrypted
D. When under automatic control

## Slide 176
G1E09 - Under what circumstances are messages that are sent via digital modes exempt from Part 97 third-party rules that apply to other modes of communication?
A. Under no circumstances
B. When messages are encrypted
C. When messages are not encrypted
D. When under automatic control

## Slide 177
G1E11 - On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations?
A. On any band segment where digital operation is permitted
B. Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands
C. Only in the non-phone Extra Class segments of the bands
D. Anywhere in the 6-meter or shorter wavelength bands, and in limited segments of some of the HF bands

## Slide 178
G1E11 - On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations?
A. On any band segment where digital operation is permitted
B. Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands
C. Only in the non-phone Extra Class segments of the bands
D. Anywhere in the 6-meter or shorter wavelength bands, and in limited segments of some of the HF bands

## Slide 179
G2E03 - What symptoms may result from other signals interfering with a PACTOR or VARA transmission?
A. Frequent retries or timeouts
B. Long pauses in message transmission
C. Failure to establish a connection between stations
D. All these choices are correct

## Slide 180
G2E03 - What symptoms may result from other signals interfering with a PACTOR or VARA transmission?
A. Frequent retries or timeouts
B. Long pauses in message transmission
C. Failure to establish a connection between stations
D. All these choices are correct

## Slide 181
G2E10 - Which of the following is a way to establish contact with a digital messaging system gateway station?
A. Send an email to the system control operator
B. Send QRL in Morse code
C. Respond when the station broadcasts its SSID
D. Transmit a connect message on the station's published frequency

## Slide 182
G2E10 - Which of the following is a way to establish contact with a digital messaging system gateway station?
A. Send an email to the system control operator
B. Send QRL in Morse code
C. Respond when the station broadcasts its SSID
D. Transmit a connect message on the station's published frequency

## Slide 183
G8C06 - What action results from a failure to exchange information due to excessive transmission attempts when using an ARQ mode?
A. The checksum overflows
B. The connection is dropped
C. Packets will be routed incorrectly
D. Encoding reverts to the default character set

## Slide 184
G8C06 - What action results from a failure to exchange information due to excessive transmission attempts when using an ARQ mode?
A. The checksum overflows
B. The connection is dropped
C. Packets will be routed incorrectly
D. Encoding reverts to the default character set

## Slide 185
G8C14 - Which of the following describes a waterfall display?
A. Frequency is horizontal, signal strength is vertical, time is intensity
B. Frequency is vertical, signal strength is intensity, time is horizontal
C. Frequency is horizontal, signal strength is intensity, time is vertical
D. Frequency is vertical, signal strength is horizontal, time is intensity

## Slide 186
G8C14 - Which of the following describes a waterfall display?
A. Frequency is horizontal, signal strength is vertical, time is intensity
B. Frequency is vertical, signal strength is intensity, time is horizontal
C. Frequency is horizontal, signal strength is intensity, time is vertical
D. Frequency is vertical, signal strength is horizontal, time is intensity

## Slide 187
Next Week
Chapter 7.1-7.4